## Slide 1: QUALITY ASSURANCE OF LARGE AREA RPC DETECTOR : TECHNIQUES FOR MEASUREMENT OF GAS LEAK RATE By Avinash V. Joshi Alpha Pneumatics , Mumbai (India)

## Slide 2: INO Project
27000 RPCs ( 2mX2m) to be used
Detector stacks are located in extremely tight space
Large volume of gas mixture used ( 216 m3)
Gas leak is serious hazard in confined space
Control over gas leak is to ensure the success of close loop gas recirculation system

## Slide 3: Effects of gas leak through RPCs
Loss of gas
Contamination by Moisture, Oxygen and other impurities
Crossing TLV for R134a and SF6
Hazardous working conditions for personnel
Loss of performance of RPC Detectors
Reduction in life of RPC Detectors

## Slide 4
Where J= the flux ( mol/m2 .sec)
D = Diffusivity of the material (m2/sec)
Φ = Concentration of material (mol/m3)
x = distance along x direction (m)
  By Fick’s First Law of Diffusion
Diffusion of contaminants into RPC

## Slide 5: Diffusion of contaminants into RPC
By applying Fick’s Second law of diffusion to one dimensional diffusion from an infinite source we get:
By applying Taylor Series approximation to (2):

## Slide 6: Glasses , support and leak path

## Slide 7: Representation of a leak
As Flow rate through fine capillaries
Where

## Slide 8: Representation of a Leak

## Slide 9: Aim : Leak rate control
Quantitative Definition of “ Acceptable range of leak rate” for 2 m x 2m glass RPCs
Reliable testing method for Acceptable leak rate , Highly Sensitive and Time Accelerated
Equipment and Procedure for measuring leak rate
RPC Production techniques to ensure high yield of RPCs with acceptable leak rate at reduced uncertainty

## Slide 10: Leak rate and the related factors
Mass leak rate is an absolute independent of gas pressure and temperature.
Leak rates of systems working at different operating conditions can be compared and evaluated, if expressed in mass leak rate.
Volume leak rate is simple to measure and can be converted to mass leak rate by :
PV = nRT to Standard conditions (273K,1BarA)
Measuring units of leak rate are : SCCM , torr*litres/sec.

## Slide 11: Operational parameters for flow through RPC
Flow
pressure
Stagnation : non-uniformity
Uniform ratio of gases throughout cavity.
Ease of Flushing in and out

## Slide 12: Case (1) : velocity distribution (m/s) for 1mX1m RPC , 0.2 Volume changes/day

## Slide 13: Case (2) : velocity distribution (m/s) for 1mX1m RPC , 0.5 Volume changes/day

## Slide 14: Criteria for Acceptable leak rate
Criteria varies for every application
Typical considerations for rpc :
i) Open ended systems : 1% of Average flow rate
Flow rate depends on volume changes/day
and volume changes/day depend upon generation of
contamination ( Radicals)
ii) Extent of contamination ingress , a function of Leak rate ,
stratification and vol. changes/day ,generation rate of
contamination and also tolerance level to Radical concentration
iii) Closed loop recirculation system :
The time interval between complete discharge of one volume change should be 6 months, in absence of Radicals.

## Slide 15: Estimate of leak rate
Internal volume of 2m X 2m RPC =8000 cc
Minimum number of Volume changes /day = 0.2 under cosmic radiation.
Total volume of gas discarded to atmosphere = 0.2 X 8000 = 1600 cc/day in open mode
A close loop system is ideally required to save 99%
Acceptable wastage rate = 16 cc/ day
Contaminant Flushing rate will be 8 cc/day
Allowable leak rate per RPC = 8 cc/day

## Slide 16: Acceptable Leak rate value
Effective total leakage :(27000 X 8 /1000 )=216 Litres/day
Equivalent to leaking 1 Kg of R134a /day @ 12 Euro /day
8 ml leak in ( 24X60X60) seconds = 10E-4 cc /sec. or 1.3 *10E-4 torr*litres /sec
Equivalent to 60 X 10E-4 SCCM

## Slide 17: Comparison of leak testing methods Limit of minimum sensitivity , Unit : torr*ltr/sec.
SN | Method | Description | Effective Range | Problem
1) | Wet Bubble Test | Water immersion | 10E-2 | Wet, point test
2) | Acoustic | Quality of sound produced by leak | 10E-3 | Local test
3) | Cumulative bubble test | Snoop type soap used to integrate leakage quantity | 10E-4 | Local test
4) | Pressure Decay | Monitoring loss of pressure with time | 10E-3 | Gross test
5) | Gas sniffer | Measure leak rate of standard gas : Moisture | 10E-4 | Purging time large, Gross test ???
6) | Gas sniffer | Exothermic gas | 10E-5 | High Sensitivity ,Gross test ???
7) | Dye Penetration | Colouring of leak point | 10E-6 | Access on both side required, long test time
8) | Helium Leak test | Mass Spectrometry | 10E-10 | High Vacuum required
9) | Isotope Tracer | Similar to sniffer | 10E-11 | Hazardous

## Slide 18: Accelerated Leak test
Acceleration by using faster gas
Hydrogen is best contender for accelerated leak test
due to its low density , low viscosity , high diffusivity and
Low background concentration in air
Under laminar flow conditions Hydrogen leaks nearly
10 times faster than R134a or SF6,
and about twice faster than Isobutane.
Under turbulent flow conditions , same ratio will be 7 and
5.5 respectively
Hydrogen sniffers with exothermic catalysts have excellent
sensitivity even at 1 ppm
Hydrogen diluted by Inert gas ( H2+ Ar) at 1% is very safe
to handle
Acceleration by using higher Pressure difference
Under higher than operating pressure difference a leak
will be faster by ratio of √ (∆P1/∆P2)

## Slide 19: Equation for Gas Leak

## Slide 20: Strain over glass plate at 0.2 BarG pressure

## Slide 21: Properties of gases
S.N. | GAS | Mol. Wt | Viscosity cP | Diffusivity in Air 10E-6 m2/sec
1) | Argon | 40 | 0.02099 | 11
2) | Isobutane | 58 | 0.0068 | 96.4
3) | Freon R134a | 102 | 0.034 | 10
4) | Oxygen | 32 | 0.02018 | 14
5) | H2O vapour | 18 | 0.013 | 24
6) | Nitrogen | 28 | 0.017 | 13
7) | Sulphur Hexafluoride | 146 | 0.014 | 8
8) | Hydrogen | 2 | 0.0087 | 78

## Slide 22: Comparison of Leak rates of gases
IF Leak rate of Freon R134a , under certain conditions, is considered as 10 units then under same conditions :
1) Isobutane will have leak rate : 50 units
2) SF6 leak rate will be slowest : 3 units.
Hydrogen will have fastest leak rate more than 100 units
4) H20 from Air will diffuse into the RPC , against differential pressure , under influence of strong concentration gradient

## Slide 23: Comparison Between Pressure decay and Sniffer test under pressure
When 1 SCCM R134a leaks through RPC having 8000 cc volume and at 1020 mBar ,the pressure drop = 1020-1019.875 = 0.125 mBar in a minute
If 55 *10E-4 SCCM gas leaks through RPC under same condition the pressure drop will be 6.8 X10E-4 / minute or 1 mBar in 1470 minutes , or one day
One millibar Pressure change in a sealed RPC can also occur due to Atmospheric pressure changes over a day-night cycle or 0.3 C change in the ambient temperature.
The pressure tranducer will not be able to measure leak rate in 10E-4 SCCM range.
On the other hand the equivalent H2 inward leak rate is at least 20 times faster and equal to 1000 10E-4 SCCM or 10E-1 SCCM
10E-1 SCCM Hydrogen in purge Argon flow of 100 SCCM = 1000 ppm which is 1000 times more than the sensitivity of Hydrogen sensor.

## Slide 24: Matheson 8057 Leak sniffer

## Slide 25: Automated Leak Test Bench for RPCs

## Slide 26: Transfer and test system for 1m X 1m detector

## Slide 27: Acknowledgements
Prof. Aniruddha Pandit and Prof Gaikar Dept. of Chemical Engineering ICT Mumbai , India
for CFD modeling of velocity distribution in RPCs