## Slide 1: Status REPORT on ICAL electronics
B.Satyanarayana, TIFR, Mumbai

## Slide 2: ICAL detector and construction
Magnet coils
RPC handling trolleys
Total weight: 50Ktons
4000mm2000mm
56mm low carbon iron sheets

## Slide 3: RPC in the ICAL detector
RPC
Iron absorber
Gas, LV & HV

## Slide 4: Factsheet of ICAL detector
No. of modules | 3
Module dimensions | 16m × 16m × 14.5m
Detector dimensions | 48.4m × 16m × 14.5m
No. of layers | 150
Iron plate thickness | 56mm
Gap for RPC trays | 40mm
Magnetic field | 1.3Tesla
RPC dimensions | 1,950mm × 1,840mm × 26mm
Readout strip pitch | 30mm
No. of RPCs/Road/Layer | 8
No. of Roads/Layer/Module | 8
No. of RPC units/Layer | 192
No. of RPC units | 28,800 (97,505m2)
No. of readout strips | 3,686,400

## Slide 5: Schematic of a basic RPC
Glass (bakelite) for electrodes
Special paint mixture for semi-resistive coating
Plastic honey-comb laminations as pick-up panel
Special plastic films for insulation
Avalanche (streamer) mode of operation
Gas: R134a+Iso-butane+SF6 = 95.5+4.2+0.3 (R134a+Iso-butane+Argon=56+7+37)

## Slide 6: Honeycomb pickup panel

## Slide 7: Post amplifier RPC pulse profile

## Slide 8: DAQ system requirements
Information to record on trigger
  Strip hit (1-bit resolution)
  Timing (200ps) LC
  Pulse profile or Time Over Threshold (for time-walk correction). TDC can measure TOT as well.
Rates
  Individual strip background rates on surface ~300Hz
    Underground rates differ: depth, rock radiation etc.
  Muon event rate ~10Hz (The ‘blue’ book says ~2Hz)
On-line monitor
  RPC parameters (High voltage, current)
  Ambient parameters (T, P, RH)
  D.C. power supplies, thresholds
  Gas systems and magnet control and monitoring

## Slide 9: Expected data sizes and rates
Pickup strip data – 128bits
TDC data: 16 channel s (8 strips ORed), dual edges, 16 hits /ch, 16-bits - 16 x 2 x 16 x 16 = 8192bits
RPC id - 16bits
Event id - 32bits
Ambient sensors (TPH) - 3 x 16 = 48bits
Noise rate data (1 second, all channels: worst case) - 1kbps
Time stamp - 100bits
Event size - 8516bits
Assume trigger rate to be 10Hz
Estimated data rate/RPC - 85160 bps + 1kbps = 84.16kbps
Add formatters, headers etc. – 100kbps/RPC
Add data from at least 8 RPCs = 8 x 100kbps = 800kbps
No data compression or zero suppression considered.
Channel occupancy a few%

## Slide 10: Segmentation of ICAL

## Slide 11: Functional diagram of RPC-DAQ

## Slide 12: Functional diagram of FE ASIC
Amp_out
8:1 Analog Multiplexer
Channel-0
Channel-7
Output Buffer
Regulated Cascode Transimpedance Amplifier
Differential Amplifier
Comparator
LVDS output driver
Regulated Cascode Transimpedance Amplifier
Differential Amplifier
Comparator
LVDS output driver
Common threshold
LVDS_out0
LVDS_out7
Ch-0
Ch-7

## Slide 13: Features of ICAL FE ASIC
IC Service: Europractice (MPW), Belgium
Service agent: IMEC, Belgium
Foundry: austriamicrosystems
Process: AMSc35b4c3 (0.35μm CMOS)
Input dynamic range:18fC – 1.36pC
Input impedance: 45Ω @350MHz
Amplifier gain: 8mV/μA
3-dB Bandwidth: 274MHz
Rise time: 1.2ns
Comparator’s sensitivity: 2mV
LVDS drive: 4mA
Power per channel: < 20mW
Package: CLCC48(48-pin)
Chip area: 13mm2

## Slide 14: FE ASIC evaluation board

## Slide 15: An important issue on FE ASIC
Separate chips for amplifier and discriminator
Helps better to support FE for glass and bakelite versions of RPC
Also helps trying out for example, different designs for comparator. For example: CFD
Does not matter much for the FE board – it is matter of one versus two ASIC chips onboard.
Alternative: Amplifier bypass option in the current ASIC (amp+comp) chip.

## Slide 16: Scheme of RPC-DAQ controller

## Slide 17: Pulse shape monitor
Shift Register
Clock
IN
Out
“Time stretcher” GHz  MHz
Waveform
stored
Inverter “Domino” ring chain (SCA)
0.2-2 ns
Stefan Ritt, Paul Scherrer Institute
Also ANUSMRITI ASIC: 500MHz Transient Waveform Sampler
V.B.Chandratre et al (BARC)

## Slide 18: ICAL timing device
ASIC (3-stage interpolation technique) – Pooja
  The new approach is to mix and match ASIC+FPGA techniques/architectures
  To be delivered in about 6 months
FPGA (Vernier technique) – Hari
FPGA (Differential delay line technique) – Sudeshna
  The FPGA efforts will continue
  Some issues (delay matching, routing etc.) to be solved
Good and bad of an FPGA solution
FPGA is a lesser travelled path (only used in CKM experiment, Fermilab)

## Slide 19: TPH monitor module

## Slide 20: Back-end issues
VME is the ICAL’s backend standard
Global services (trigger, clock etc.), calibration
Data collector modules
Computer and data archival
On-line DAQ software
On-line data quality monitors
Networking and security issues
Remote access protocols to detector sub-systems and data
Voice and video communications
Drawings courtesy: Gary Drake

## Slide 21: VME Interface Logic
Address
Data
Addr. Modifier
Address
Decoder
Data
Router
FPGA
Front Panel Out
Front Panel In
Piggy Brd Data
Piggy Board ID
LVDS
I/O
Piggy
Board
Conn
Interrupt Gen
And Handler
256
Deep
FIFO
Int1, Int2
Interrupt Ctrl
V
M
E
B
U
S

## Slide 22: Custom VME Module
VME Interface
Logic
(FPGA)
VME Data
Transceiver
Data Bus
VME Addr
Transceiver
Address Bus
JTAG
FPGA Configuration Logic
On board logic analyser port
VME Control Signals
Buffer
AM, DS, WR, SYSRST, IACK..
Buffer
VME
BUS
LVDS Tx OUT
LVDS Rx IN
Data
Interface for V1495s piggy boards
OE
DIR
OE
DIR
DATCK, IACKOUT, IRQs, BERR
Front panel LEDs
Board Address

## Slide 23: Features of ICAL trigger system
Insitu trigger generation
Autonomous; shares data bus with readout system
Distributed architecture
For ICAL, trigger system is based only on topology of the event; no other measurement data is used
Huge bank of combinatorial circuits
Programmability is the game, FPGAs, ASICs are the players

## Slide 24: Proposed trigger scheme

## Slide 25: Power supplies
High voltage for RPCs
  Voltage: 10kV (nominal for Glass, less for Bakelite)
  Current: 6mA (approx., 200nA per chamber)
  Ramp up/down, on/off, monitoring
Low voltage for electronics
  Voltages and current budgets still not available
Commercial and/or semi-commercial solutions
  Buy supplies, design distribution( and control)?
DC-DC and DC-HVDC converters; cost considerations

## Slide 26: Cables and interconnects
RPC to front-end boards – the toughest!
  Integration with pickup panel fabrication
Front-end boards to RPC-DAQ board
  LVDS signals (any alternatives?, prefer differential)
  Channel address
  Analog pulse
  Power
RPC-DAQ boards to trigger sub-systems
  Four pairs, Copper, multi-line, flat cable?
RPC-DAQ boards to back-end
  Master trigger
  Central clock
  Data cable (Ethernet: copper/fibre, …)

## Slide 27: Other critical issues
Power requirement and thermal management
  If 50mW/channel → 200KW/detector
  Magnet power (500KW?)
  Front-end positioning; use absorber to good use!
  Do we need forced, water cooled ventilation?
  UPS, generator power requirements
    High voltage supplies, critical controls, computers on UPS
Suggested cavern conditions
  Temperature: 20±2oC
  Relative humidity: 50±5%

## Slide 28: Roll of electronics industries
Chip fabrication
Board design, fabrication, assembly and testing
Cabling and interconnects
Crates and mechanics
Slow control and monitoring
  Control and monitoring systems for gas systems and magnet
Industries (both public and private) are looking forward to work with INO

## Slide 29: Future plan
VECC, IITM, BARC groups will send reports on their work and future plans shortly.
ICAL Electronics Report needs these inputs and will be finalised soon.
ASIC and FPGA based TDC designs is the priority.
Pilot RPC-DAQ (without TDC chip) board will be developed and tested on the RPC detector stack.
VME interface development will naturally lead to development of data concentrator module
Several technical issues including many interconnects etc. to be addressed immediately
Interaction with industrial houses and figure out areas in which we can benefit by their expertise and abilities

## Slide 30: Work packages – Part 1
Signal pickup panels
RPC to front-end interconnects
Front-end
RPC-DAQ module
  TDC
  Waveform sampler
  Strip-hit latch and rate monitor
  Controller + data transreceiver
  Firmware for the above
  Pre-trigger front-end
  TPH monitoring
  Pulse width monitoring
  Front-end control
  Signal buffering scheme
Trigger system
DAQ backend

## Slide 31: Work packages – Part 2
Software
Power supplies
Power requirement and thermal management
Integration issues
  Routing of strip signals to the front-ends
  Mounting of front-ends and RPC-DAQ module on the RPC unit
  Routing of LV, HV (along with gas) lines to the RPC
  Routing of LV, HV, data, trigger lines (along with gas) on the magnet
  Locating and routing of pre-trigger lines into segment trigger stations
  Location of backend VME crates and final trigger system
  Power supplies’ mains and distribution
Production and QC
  Board and module design
  Production, QC, programming and calibration
  Cabling and connectorisation etc. (specifications decided by the collaboration)
  Crates, racks and other mechanics
Installation and commissioning
Operation considerations