## Slide 1: Development of 2m × 2m size glass RPCs for INO
M. Bhuyan1, V.M. Datar2, S.D. Kalmani1, S.M. Lahamge1, S. Mohammed3, N.K. Mondal1,
P. Nagaraj1, A. Redij1, D. Samuel1, M.N. Saraf1, B. Satyanarayana1*, R.R. Shinde1 and P. Verma1
India-based Neutrino Observatory (INO) Collaboration
1Department of High Energy Physics, Tata Institute of Fundamental Research, Mumbai 400005, India
2Nuclear Physics Division, Bhabha Atomic Research Centre, Mumbai 400085, India
3Department of Physics, Aligarh Muslim University, Aligarh 202002, India
*Corresponding author (bsn@tifr.res.in)

## Slide 2: Plan of the talk
Introduction
RPC fabrication procedure
Basic characterisation studies
Studies with SF6 gas mixtures
Summary and outlook

## Slide 3: INO cavern and the ICAL detector
Vertical rock coverage: 1300m
Magnet coils
RPC handling trolleys
Total weight: 50Ktons
4000mm2000mm low carbon iron slab

## Slide 4: Factsheet of ICAL detector
No. of modules | 3
Module dimensions | 16m × 16m × 14.5m
Detector dimensions | 48.4m × 16m × 14.5m
No. of layers | 150
Iron plate thickness | 56mm
Gap for RPC trays | 40mm
Magnetic field | 1.3Tesla
RPC dimensions | 1,840mm × 1,840mm × 24mm
Readout strip pitch | 3 0mm
No. of RPCs/Road/Layer | 8
No. of Roads/Layer/Module | 8
No. of RPC units/Layer | 192
No. of RPC units | 28,800 (97,505m2)
No. of readout strips | 3,686,400

## Slide 5: Glass electrode preparation
Glass cleaning
  Cleaned with Labolene soap solution and rinsed with distilled water
  Left to natural drying
  Wiped with iso-propyl alcohol
Spray painting
  Using auto garage compressor and paint spray gun
  Left to natural drying
  Currently scaling-up an automated paint plant used for 1m x 1m glass

## Slide 6: Surface resistivity measurement
Measurement data
  Reasonably uniform
  Needs improvement at the edges
  Better uniformity obtained on sheets painted by automatic paint plant
Measurement jig
  Developed a simple technique
  Fabricated jigs of various sizes to suit for measurements of different grid sizes

## Slide 7: 2mx2m RPC: Gas gap preparation-1
Bottom glass in place
  Template for button positions placed below the bottom glass
  Buttons placed on 20cm x 20cm grid
Gluing of buttons
  Currently glue dispensed manually
  Protective template placed on the glass
  Auto timer-based glue dispenser being designed

## Slide 8: 2mx2m RPC: Gas gap preparation-2
Placing the top glass
  Tilting the work table for placing the top glass electrode
  Precise stoppers mounted on the table for guiding the top glass
Vacuum jig for gluing
  A simple vacuum jig designed for perfect and efficient gluing of the gas gap
  Technique suggested by Carlo Gustavino

## Slide 9: 2mx2m RPC: Gas gap preparation-3
Preparing to glue bottom-side
  Rotating the work table for gluing bottom-side spacers
  Suitable work-table design and over-head crane for easy handling of glasses and gaps
Ready to glue top-side spacers
  Last step before closing the gas gap
  Gas nozzles on all four corners of the gap – two each used for gas inlet and outlet

## Slide 10: 2mx2m RPC: Gas gap preparation-4
Leak testing the gap
  The gap pressurised marginally above atmosphere with R134a gas
  Tested for leaks with R134a leak detector
  Leaks plugged
Fully fabricated gas gap
  Gap ready to be assembled as an RPC detector chamber

## Slide 11: Construction of an RPC detector
Signal reference plane.1
Plastic honey comb.2
Copper pickup strips.3
Graphite/Paint.4
Top glass.5
Button spacer.6
Bottom glass.7
Edge spacer.8
Gas nozzle.9
Bottom pickup panel.A
1
2
3
4
5
6
7
8
9
A

## Slide 12: 2mx2m RPCs in Cosmic test stand
Front-end electronics

## Slide 13: RPC pulse height studies
Mean pulse height from the RPC: 2.5-3mV
Preamplifier pulse shots
Pulse height distribution

## Slide 14: Charge and time distributions
Charge
Timing

## Slide 15: Monitoring operating parameters
Efficiency plateau
Noise rate profile

## Slide 16: SF6 studies: RPC pulse profile
SF6 = 0%
SF6 = 0.32%

## Slide 17: SF6 studies: Chamber current
V-I characteristics
Chamber current

## Slide 18: SF6 studies: Collected signal charge
Charge distributions
Charge parameters

## Slide 19: SF6 studies: Important operating parameters
Efficiency
Noise Rate

## Slide 20: SF6 studies: Timing characteristics
Time response
Time resolution

## Slide 21: Summary and outlook
Successful fabrication and characterisation of large area RPCs required for INO’s ICAL experiment
Two more 2m x 2m will be made; more detailed studies to follow
Timing studies with long pickup strips, in particular
  Poster by Deepak Samuel et al & Sumanta Pal et al
Gas systems’ studies with RGA
  Presentations by S.D.Kalmani et al & Avinash Joshi
Cascading of gas lines; optimisation of gas flow, cost considerations
Studies using new pickup panel designs, cost considerations
Essentially –
  1m x 1m RPC stack continued to be used for long-term, cosmic, tracking studies, Presentation by Naba Mondal et al
  2m x 2m RPC stand being used for optimising RPC design for industrial production and testing for ICAL operating conditions
Engineering Design Report (EDR) on large scale industrial production of RPCs needed for ICAL, is under preparation